Risk Assessment for Zip Wire

Name of Assessor: -	M Worfell	Date of Assessment: -	01/03/19

Signature of Assessor: -       	Assessment No: -	18

Operating Areas: - Calvert Trust Wall	Next Revision: -		01/03/20

| Significant Hazards | Groups Of People Who Are At Risk From The Significant Hazard | Existing Controls And Advisory Guidelines | Notes |
| --- | --- | --- | --- |
| Slips and trips. Uneven ground. Trailing ropes and slings. Step from launch area surface. Steps up from landing area. | All staff and participants | Comprehensive safety and operating brief, prior to and during activity. Controlled access to risk area. Close supervision of participants during active and passive phases of activity. Use ramped route to top of zip to avoid high steps. | The launch area needs regular checks to ensure the matting remains flat and even. |
| Equipment failure. | All staff and participants | Each use visual check on cable clamps, anchors and carriage. Cable to be greased regularly Formal checks at regular intervals and written record kept, especially wear under springs. Use of appropriately experienced instructors. Use of appropriate rope and hoist system with safety backup system. Always use safety clip back as well as quick release whilst hoisting participant until safety has been attached. Zip sag is verified prior to every session. | Annual checks done by Safety Equipment Engineer |
| Head hitting carriage or rope system. | Participants | Constant attention to safe practice. Structured and disciplined working method. All participants wear a climbing helmet where appropriate. New wrap around pad fitted prior to release. | Glasses to be removed if appropriate. Pad applied. |
| Collision of user with other users or staff | All staff and participants | Close supervision of participants. Clear indication of safety areas to be given to users. Ensure only instructional staff use the stepped path by the tower. | Staff to set up simple communication system between each other to ensure it is safe to proceed up steps or send guest down zip. |
| Exposure to extremes of temperature. Low & High | All staff and participants | Full equipment brief prior to activity and provision of spare clothing where necessary. Provision of shade, shelter and fluids. Attention to be paid to variations in cable length as a result of expansion/shrinkage in hot cold weather | We encourage participants to present themselves prepared for a day outside by consuming adequate food before and during activity, taking appropriate medication and informing us of any illness, which may inhibit their ability to partake. Without this co-operation, participants and their carers are potentially exposed to greater risks. |
| Grabbing Wire whilst in motion | Participants | Gloves supplied when there is a suspected possibility of grabbing wire. First decent will be tailed by instructor for any participant deemed liable to grab at the wire. |  |
| Feet snagging on ground during launching and in flight. | Participants who are either tall or heavy with poor mobility. | Use paraponte harness or a carer to support the legs. Send user backwards. Vegetation cut back regularly. | Maintain attention to height of wire during hot weather and after periodic stretching during the season. |
| Manual Handling | Staff | Weight Limit specified Steps/box used to minimise lifting where possible Get assistance from other group members Close supervision of participants. Correct use of equipment provided. |  |
| Moving and Handling | Staff and participants | All activity leaders to receive initial, then ongoing manual handling training. Supported by Moving and Handling in the outdoors training DVD. These along with the medical notes form the basis of a consultative approach to movement with close supervision specific to the session. |  |